## Slide 1: MIKEY-IBAKE and LI Approaches

## Slide 2: Introduction
  MIKEY-IBAKE was included in TR 33.829 at the last SA3 meeting
  PRG approach for LI for MIKEY-IBAKE was discussed at the last SA3 LI meeting
    Open issues discussed in a separate contribution
  This contribution discusses several available alternatives for LI with MIKEY-IBAKE.

## Slide 3: Discovery of MIKEY-IBAKE Session Keys
MIKEY-IBAKE session key SK
  SK = xyP
    P is known point on a known elliptic curve
    x and y are random numbers generated at A and B
      X and y are known only to A and B, respectively
    IBE encrypted Key Components xP and yP are exchanged between A and B.
    A and B decrypt received Key Components and compute SK = x*yP = y*xP
  Multiple ways to obtain x and/or y
  Re-generate x and/or y
  Exchange encrypted x/y during MIKEY-IBAKE exchange

## Slide 4: LI approaches for MIKEY-IBAKE
Based on MIKEY-IBAKE use case scenarios there are multiple ways to perform Lawful Intercept for MIKEY-IBAKE
  Consolidated PRG approach
  Split PRG approach
  Consolidated nonce approach
  Split nonce approach
Different approaches resulting from different deployment scenarios provide different properties (e.g., elimination of key escrow, perfect forward secrecy, etc.)

## Slide 5: A. Consolidated PRG Approach
A
KMS
B
MIKEY-IBAKE
CSCF
Provider’s Database
Random Secret Generation
PRG seeds SA/SB are pre-provisioned in a mobile and Provider’s Database consolidated with KMS.
Secret x/y is generated using PRG of Seed S and a Time Stamp T of the first MIKEY message.
Session Key Discovery
DF sends MIKEY-IBAKE messages to KMS and requests Session Key
KMS re-generates the random secret, decrypts MIKEY messages to obtain the key components, and computes the Session Key
x = PRG(SA, T)
y = PRG(SB, T)
LEMF
ADMF
Delivery
function
X1_1
X1_2
X2
Xk
Notes: <number>

## Slide 6: B. Split PRG Approach
A
KMS
B
MIKEY-IBAKE
CSCF
Provider’s Database
Random Secret Generation
PRG seeds SA/SB are pre-provisioned in a mobile and Provider’s database.
  Illustration above shows Provider’s Database split from KMS
Secret x/y is generated by PRG using Seed S and a Time Stamp T
Session Key Discovery
DF obtains target’s secret x or y from Provider’s Database and target's IBE Private Key from KMS
DF uses IBE Private Key to decrypt MIKEY-IBAKE messages and obtain missing Key Component.
Using Key Component and Target’s secret, the DF generates the session key
x = PRG(SA, T)
y = PRG(SB, T)
LEMF
ADMF
Delivery
function
X1_1
X1_2
X2
Xk
Notes: <number>

## Slide 7: Nonce-Based Approach
A
B
Public key of A (PUB_A)
Public key of B (PUB_B)
A, B, IBE(A|B|xP|A_Nonce)PUB_B
Chooses random x and computes xP
Computes A_Nonce
Decrypts the message using PR_B
Chooses random y and computes yP
Computes B_Nonce
B, A, IBE(B|A|xP|yP|A_Nonce|B_Nonce)PUB_A
A, B, IBE(A|B|yP|B_Nonce)PUB_B
Decrypts the message using PR_A and verifies received xP
Verification
Private key of A (PR_A)
Private key of B (PR_B)
P - Public parameter: a publicly known point on a known elliptic curve
  A_Nonce == AESA_MASTERSECRET(x)
  B_Nonce == AESB_MASTERSECRET (y)
  Corresponding nodes treat Nonces simply as random Cookies
A_Mastersecret
B_Mastersecret

## Slide 8: C. Consolidated Nonce-Based Approach
A
KMS
B
MIKEY-IBAKE
CSCF
MASTERSECRET known only to A/B and KMS
MASTERSECRET provisioned into User A/B by KMS (e.g., once a month at the time IBE Private Keys are exchanged)
Session Key Discovery
DF sends MIKEY-IBAKE messages to KMS and requests Session Key
KMS decrypts corresponding Nonce and obtains x/y
KMS generates the Session Key and sends it to DF
A_Nonce = AESA_MASTERSECRET(x)
B_Nonce = AESB_MASTERSECRET(y)
LEMF
ADMF
Delivery
function
X1_1
X1_2
X2
Xk

## Slide 9: D. Split Nonce-Based Approach
A
KMS
B
MIKEY-IBAKE
CSCF
Provider’s Database
MASTER SECRET
A_MASTERSECRET and B_MASTERSECRET are pre-provisioned in a mobile and Provider’s database
  MASTERSECRET not known to the KMS
Session Key Discovery
DF obtains target's Private Key from KMS
  DF uses IBE Private Key to decrypt MIKEY-IBAKE messages to obtain key component and target’s Nonce.
DF sends the Target’s Nonce to Provider’s Database and receives decrypted Target’s Secret x/y.
Using key component and received Target’s secret, the DF generates the Session Key
LEMF
ADMF
Delivery
function
X1_1
X1_2
X2
Xk
A_Nonce = AESA_MASTERSECRET(x)
B_Nonce = AESB_MASTERSECRET(y)

## Slide 10: Summary
Multiple LI approaches for MIKEY-IBAKE
  All approaches satisfy LI requirements relating to the use of operator applied encryption as specified in TS 33.106
  Different approaches result in different properties