## Slide 1: MIKEY-IBAKE and LI - Open Issues

## Slide 2: Introduction
  Pseudo Random Number Generator approach for LI for MIKEY-IBAKE was discussed in the last SA3 LI meeting
  This contribution discuses open issues brought up during last meeting

## Slide 3: Discovery of MIKEY-IBAKE Session Keys
MIKEY-IBAKE session key
  SK = xyP
    P is known point on a known elliptic curve
    x and y are output of a Pseudo-Random Number Generator (PRG) invoked at I and R

## Slide 4: Discovery of Session Key with Re-Generation of Secret
I
KMS
R
MIKEY-IBAKE
CSCF
Provider’s Database
Session Key Discovery
PRG seeds SI/SR are pre-provisioned in a mobile and Provider’s database.
  Illustration above shows provider’s database consolidated with KMS
Secret x/y is generated by PRG using S and a Time Stamp
  x/y can be re-generated by Enterprise Server using S and Time Stamp
Intercepting NE obtains Session Key from the KMS
x = PRG(SI, T)
y = PRG(SR, T)
LEMF
ADMF
Delivery
function
X1_1
X1_2
X2
Xk
Notes: <number>

## Slide 5: Discovery of Session Key with Re-Generation of Secret
I
KMS
R
MIKEY-IBAKE
CSCF
Provider’s Database
When LI has been activated in the P/S-CSCF, the node will report SIP messages events on the X2 interface
The DF/MF shall extract from the intercepted SIP signalling the information related to the encryption and send a request over the Xk interface to the KMS to derive the session keys;
x = PRG(SI, T)
y = PRG(SR, T)
LEMF
x = PRG(SI, C)
ADMF
Delivery
function
X1_1
X1_2
X2
Xk
Notes: <number>

## Slide 6: Open Issues
Issues brought up during last meeting relate to the fact that random secret (e.g., x) is generated using Counter value or a Timestamp
  Philadelphia draft report_v0_2.doc:
    “The solution seems to depend on time synchronisation of UEs which may be difficult to achieve in practice. He felt multiple keys may be needed to allow for uncertainties. He also raised the issue of roamers who may be on different time zones to the visited network.”
  RESOLUTION
Use the value used to populate Timestamp payload for the generation of the random secret
MIKEY_IBAKE messages are communicated to the KMS, therefore KMS has the exact Timestamp for the generation of the random secret

## Slide 7: Use of the Timestamp
MIKEY-IBAKE exchange as specified in RFC 6267
All exchanges include Timestamp payload
  The timestamp payload carries the timestamp information
Initiator
Responder
I_MESSAGE_1 = HDR, T, RAND, IDRi, IDRr, IBAKE, [ESK]
R_MESSAGE_1 = HDR, T, IDRi, IDRr, IBAKE
I_MESSAGE_2 =HDR, T, RAND, IDRi, IDRr, IBAKE, [ESK]
R_MESSAGE_2 = HDR, T, [IDRi], [IDRr], [IBAKE], V